## Slide 1
The CS and CE amplifier with current-source loads
Active-load CS amplifier (biased to operate in the saturation region):
Equivalent circuit
Intrinsic gain
Intrinsic gain is only 20 to 40 V/V for a MOSFET in a modern short-channel technology
For a given technology: larger A0 as VOV decreases and L increases
For a given transistor: larger A0 increases as VOV and ID decrease
The Basic Gain Cell
Gain levels off at very low currents as the MOSFET enters the subthreshold region operation where it becomes similar to a BJT with an exponential current-voltage characteristics
Notes: VA = Early voltage; thermal voltage VT;
V’A is the technology-dependent component of the Early voltage.
VOV is a design parameter, is still about 0.15 V to 0.3 V.
.

## Slide 2
Active-load CE amplifier (biased to operate in the active region):
Equivalent circuit
Intrinsic gain
Maximum gain obtainable in a CE amplifier (assuming an ideal dc current source)
Technology-determined parameter
Independent of the transistor junction area and the bias current for a given fabrication process
VA ranges from 5 to 35 V for modern IC fabrication process
VA ranges from 100 to 130 V for high-voltage process
Intrinsic gain ranges from 200 to 5000 V/V
The Basic Gain Cell

## Slide 4: Example 1
We wish to compare the values of gm, Rin, R0, and A0 for a CS amplifier that is designed using an NMOS transistor with L = 0.4 μm and W = 4 μm and fabricated in a 0.25-μm technology specified to have μnCox = 267 μA/V2 and V’A = 10V/μm, with those for a CE amplifier designed using a BJT fabricated in a process with  = 100 and VA = 10 V. Assume that both devices are operating at a drain (collector) current of 100 μA.

## Slide 5: Example 1 solution
For simplicity, we shall neglect the Early effect in the MOSFET in determining V0V, thus:
resulting in
For the CE amplifier we have

## Slide 6: Effect of the Output Resistance of the Current-Source Load
The current-source load of the CS amplifier in Figure (b) can be implemented using a PMOS transistor biased in the saturation region to provide the required current I, as shown in Figure (a).
Figure (a)
Figure (b)
The current source can be realized by using a PMOS in saturation

## Slide 7
Figure (a): The CS amplifier with the current-source load implemented with a p-channel MOSFET Q2 ; (b) the circuit with Q2 replaced with its large-signal model; and (c) small-signal equivalent circuit of the amplifier.
Effect of the Output Resistance of the Current-Source Load

## Slide 8: Effect of the Output Resistance of the Current-Source Load
The output resistance is no longer infinite due to channel-length modulation
The voltage gain is reduced due to the finite output resistance of the current-source load.
The gain is reduced by half if Q1 has the same Early voltage as Q2 does (ro1= ro2)
Voltage gain of the CS amplifier with a current-source load

## Slide 9
Quiz 2.2
You submit your solution not later than March 20, 2020.
You can submit through Blackboard as informed by Mr. Huy on Blackboard announcement.
Reuse all data given and obtained in Quiz 2.1.
Plot small signal equivalent circuit.
Determine voltage gain vo/vi.
Compute output impedance of the circuit.