## Slide 1: Increasing the Gain of the Basic Cell
Q: How can we increase the voltage gain obtained from basic gain cell?
  A: Find a way to raise the level of output resistance of the gain cell. The gain is proportional to the resistance at the output
  A: Seek a circuit that passes the current gmvi provided by the amplifying transistor right through, but increases the resistance from ro to a much larger value.
  The only candidate is CG or CB amplifier
Figure: To increase the voltage gain realized in the basic gain cell shown in (a), a functional block, shown as a black box in (b), is connected between d1 and the load.

## Slide 2: Increasing the Gain of the Basic Cell
The black box of Figure is a current buffer
Two important observations should be made:
  It is not sufficient to raise output resistance of amplifying transistor only.
  Placing CG (or a CB) circuit on top of the CS (or CE) amplifying transistor to implement the current-buffering action is called cascading.

## Slide 3: The Cascode Amplifier
Cascoding refers to the use of the transistor connected in the common-gate (or common-base) configuration.
Provides current buffering for the output of a common-source (or common-emitter) amplifying transistor.
Figure in the next slide illustrates this technique for MOS case.
The MOS cascode

## Slide 4: The Cascode Amplifier
Circuit topology:
  Putting a CG (Q2:cascode transistor  current-buffering action is implemented using a transistor Q2 ) on top of CS (Q1:amplifying transistor). Here VG2 is the dc bias voltage.
  The cascode transistor passes the small-signal current gm1vi to the output node while raising the resistance level by a factor of K

## Slide 5: The MOS Cascode
Figure: (a) A MOS cascode amplifier prepared for small-signal calculations; (b) output equivalent circuit of the amplifier in (a); (c) the cascode amplifier with the output short-circuited to determine Gm; (d) equivalent circuit of the situation in (c).
Figure shows the MOS cascode amplifier without a load circuit and with the gate of Q2 connected to signal ground.
  This circuit is valid for small-signal calculations only.
Objective is to determine the parameters gm and RO of the equivalent circuit shown in Fig (b).
If the node d2 of the equivalent circuit is short-circuited to ground, the current flowing through the short-circuit will equal Gmvi.
  Note that Gm = io/vi.

## Slide 6
Observe that the voltage at the (d1, s2) node is equal to –vgs2. Writing a node equation for that node, we have
The current of the controlled source of Q2 is equal to that of the controlled source of Q1
@ d2 node:
Thus:
The MOS Cascode

## Slide 7
The MOS Cascode
@ the source node of Q2
vx is the sum of the voltages across ro2 & ro1 as
The CG transistor Q2 raises the output resistance of the amplifier by the factor gm2ro2
At the same time, Q2 simply passes the current gm1vi to the output node.
Thus the CG or cascode transistor very effectively realizes the objectives we set for the current buffer with
K = Ao2 = gm2ro2
Figure: Determining the output resistance of the MOS cascode amplifier.

## Slide 8
Quiz 2.3
Two NMOS FETs Q1 and Q2 are depicted in the Figure. The current ID = 0.5mA for both transistors, and VGS – Vt = 1V for Q1 and Q2. The value RD = 4kΩ and VA = 100V for Q1 and Q2.
What is the name of this circuit?
Determine ro1 and ro2.
Plot small signal equivalent circuit. Compute Gm and Ro.
Determine voltage gain vo/vi.
You submit your solution not later than March 20, 2020.
You can submit through Blackboard as informed by Mr. Huy on Blackboard announcement.
Positive voltage
D
Q2
Q1
Negative voltage
D
S
S