## Slide 1: Double Cascoding
If still a higher output resistance and correspondingly higher gain are required, it is still possible to add another level of cascoding – as illustrated in Figure.
Observe that Q3 is the second cascode transistor, and it raises the output resistance by (gm3ro3).
Figure: Double cascoding.
Even higher output resistance can be achieved in MOSFET circuits by double cascoding
Requires higher supply voltage as one more CG transistor is stacked in the gain stage
Double cascoding is required for the current-source load to realize the advantage in voltage gain
Drawback of double cascoding!

## Slide 2: The Folded Cascode
To avoid the problem of stacking a large number of transistors across a low-voltage power supply, one may use a PMOS transistor for the cascode device – as shown in Figure.
This provides an alternative to the design proposed in previous section.
Figure: The folded cascode.
The dc current of Q2 is I2 and the current of Q1 is (I1 - I2)
The voltage limitation due to stacking of NMOS transistors can be alleviated
Small-signal operation is similar of NMOS cascode

## Slide 3
The BJT Cascode
Fig (a): the BJT cascode amplifier with an ideal current-source load.
Voltage VB2 is a dc bias voltage for the CB cascode transistor Q2.
Objective is to determine the parameters Gm and Ro of the equivalent circuit of Fig (b).
As in case of MOS cascode, Gm is the short-circuit transconductance and can be determined from the circuit in Fig (c).

## Slide 4: The BJT Cascode
Let’s determine the parameters Gm and Ro of the equivalent circuit.
The transconductance Gm = io / vi
Replacing Q1 and Q2 with their hybrid-  equivalent-circuit models
Since gm2 ≫ (1/r2), 1/ro1, and 1/ro2,
A node equation at c2 is

## Slide 5
The BJT Cascode
Open-circuit voltage gain of the bipolar cascode:

## Slide 6
Figure: A BJT cascode amplifier with a cascode current source.
The BJT Cascode
Note that to realize gains approaching this level, the current-source load must also be cascoded.
which will be less than (gmro)2 in magnitude. In fact, the maximum possible gain magnitude is obtained when ro >> r and is given by

## Slide 7: The Output Resistance of an Emitter-Degenerated CE Amplifier
As done in MOS case, one may adapt the expression for Ro derived from BJT cascode.
For the case of a CE amplifier with Re as shown in Figure (a).
The output resistance is
(a)

## Slide 8
Quiz 2.5
The simplified cascode amplifier used in the theory is shown in the Figure. The current I = 1mA. Two transistor are identical with β = 100 and VA = 50V.
Determine rπ1 and rπ2.
Determine ro1 and ro2.
Determine gm1 and gm2.
If the output resistance of the current source (I) is 200kΩ, plot the small signal equivalent circuit.
Compute the voltage gain vo/vi.
You submit your solution not later than March 20, 2020.
You can submit through Blackboard as informed by Mr. Huy on Blackboard announcement.