## Slide 1: IC Biasing – Current Sources, Current Mirrors, and Current-Steering Circuits
Biasing in integrated-circuit design is based on the use of constant-current sources.
  On an IC chip with a number of amplifier stages, a constant dc current (reference current) is generated at one location and is then replicated at various other locations for biasing.
    This is known as current steering.
This approach has the advantage that the effort expended on generating a predictable and stable reference current need not be repeated.

## Slide 2: The Basic MOSFET Current Source
Figure shows the circuit of a simple MOS constant-current source.
The heart of the circuit is transistor Q1, the drain of which is shorted to the gate, thereby forcing it to operate in saturation mode.
The drain current of Q1 is supplied by VDD through resistor R which in most cases is located outside of the IC chip.
If one considers transistor Q2, it is realized that it has VGS identical to Q1
Figure: Circuit for a basic MOSFET constant-current source. For proper operation, the output terminal, that is, the drain of Q2, must be connected to a circuit that ensures that Q2 operates in saturation.
Consider transistor Q2
Widely used for ICs with good device matching

## Slide 3: The Basic MOSFET Current Source
Figure: Basic MOSFET current mirror.
The combination of Q1 and Q2 is referred to as a current mirror.
Figure depicts the current-mirror circuit with the input reference current shown as being supplied by a current source for both simplicity and generality.
The current gain or current transfer ratio of the mirror is given by (*).
The effect of Vo on Io is defined in equations :
(*)
To ensure that Q2 is saturated VO ≥ VGS – Vtn
The output resistance:
VA2 is the Early voltage of Q2
We can express the current Io

## Slide 4
Figure: Output characteristic of the current source and the current mirror for the case of Q2 matched to Q1.
The Basic MOSFET Current Source

## Slide 5: Example
Given VDD = 3V and using IREF= 100μA, design the circuit of Fig. to obtain an output current whose nominal value is 100 μA. Find R if Q1 and Q2 are matched and have channel lengths of 1 μm, channel widths of 10 μm, Vt = 0.7 V and k’n = 200 μA/V2. What is the lowest possible value of Vo? Assuming that for this process technology, the Early voltage V’A = 20 V/μm, find the output resistance of the current source. Also, find the change in output current resulting from a +1-V change in Vo.

## Slide 6: Example - Solution
For the transistors used, L = 1 μm.
The output current will be 100 μA at Vo = VGS = 1V. If Vo changes by +1 V, the corresponding change in Io will be

## Slide 7: MOS Current-Steering Circuits
Once a constant current has been generated, it can be replicated to provide dc bias or load current for the various stages of the amplifier in an IC.
Current mirrors can be used to achieve this goal.
Current sink: pulls a dc current from a circuit
Current source: pushes a dc current into a circuit
All transistors should be operated in saturation
Current mismatch exists for a finite VA (channel-length modulation)

## Slide 8
Figure: A current-steering circuit.
MOS Current-Steering Circuits
Transistors Q1, Q2, and Q3 form a two-output current mirror.
To ensure operation in the saturation region VD2, VD3 ≥ –VSS +VGS1 −Vtn
Current I3 is fed to the input side of a current mirror formed by PMOS transistors Q4 and Q5.
where I4 = I3. To keep Q5 in saturation
VD5 ≤ VDD − |VOV5|

## Slide 9
Figure: A current-steering circuit.
Important note is that in the circuit, while Q2 pulls its current I2 from a circuit (not shown in Fig.), Q5 pushes its current I5 into a circuit (not shown in Fig.). Thus Q5 is appropriately called a current source, whereas Q2 should more properly be called a current sink. In an IC, both current sources and current sinks are usually needed.

## Slide 10: BJT Circuits
The basic BJT current mirror is shown in Fig.
It works in a fashion very similar to the MOS mirror. However, with two important differences:
  The non-zero bias current causes an error in current mirroring (magnitude of current conducted).
  The current transfer ratio is determined by the relative areas of the emitter-based junctions of Q1 and Q2.
The textbook provides a more detailed description of the BJT-based current mirror – including equations which correspond to those provided for MOS-based mirror.
Figure: The basic BJT current mirror.

## Slide 11
BJT Circuits
Figure: Analysis of the current mirror
taking into account the finite β of the BJTs.

## Slide 12
BJT Circuits
Figure: A simple BJT current source.

## Slide 13
BJT Circuits
Current Steering
Figure: Generation of a number of constant currents of various magnitudes.
Q3 will supply a constant current I equal to IREF .
Two transistors, Q5 and Q6 are connected in parallel, and the combination forms a mirror with Q1. Thus I3 = 2IREF .
Constant current I2 equals to IREF .
Finally, to generate a current three times IREF , three transistors, Q7,Q8 and Q9, each of which is matched to Q2, are connected in parallel.

## Slide 14
  A Bipolar Mirror with Base-Current Compensation
Base-current compensation by an additional transistor Q3
The current transfer ratio is much less dependent on 
Output resistance Ro  ro2
Current-Mirror Circuits with Improved Performance

## Slide 15
Figure: The Widlar current source.
  The Wildar Current Source
    A resistor RE is included in the emitter lead of Q2.
Allows the generation of a small constant current using relatively small resistors
Advantageous in considerable savings in chip area for integrated circuits
Neglecting base currents we can write as:
Output resistance is

## Slide 16: Example
Fig. shows two circuits for generating a constant current IO = 10μA which operate from a 10-V supply. Determine the values of the required resistors assuming that VBE is 0.7V at a current of 1 mA and neglecting the effect of finite .

## Slide 17: Example - Solution

## Slide 18: Summary
Integrated-circuit fabrication technology offers the circuit designer many exciting opportunities, the most important of which is the large number of inexpensive small-area MOS transistors. An overriding concern for IC designers, however, is the minimization of chip area or “silicon real estate.” As a result, large-valued resistors and capacitors are virtually absent.
The basic gain cell of IC amplifier is the CS (CE) amplifier with a current-source load. For an ideal current-source load (i.e. one with infinite output resistance), the transistor operates in an open-circuit fashion and thus provides the maximum gain possible: Avo = -gmro = -A0.

## Slide 19: Summary
The intrinsic gain A0 is given by A0 = VA / VT for a BJT and A0 = VA/(VOV/2) for a MOSFET. For a BJT, A0 is constant independent of bias current and device dimensions. For a MOSFET, A0 is inversely proportional to ID1/2. See equation 7.15.
Simple current-source loads reduce the gain realized in the basic gain cell because of their finite resistance (usually comparable to the value of ro of the amplifying transistor).
To raise the output resistance of the CS or CE transistor, we stack a CG or CB transistor on top. This is cascoding. The CG or CB transistor in the cascode passes the current gm1vi provided by the CS or CE transistor.

## Slide 20: Summary
A MOS cascode amplifier operating with an ideal current source load achieves a gain of (gmro)2 = A02.
To realize the full advantage of cascoding, the load current-source must also be cascoded, in which case a gain as high as 1/2A02 can be obtained.
Double cascoding is possible in the MOS case only. However, the large number of transistors in the stack between the power-supply rails results in the disadvantages of a severely limited output-signal swing. The folded-cascode configuration helps to resolve this issue.

## Slide 21: Summary
A CS amplifier with a resistance Rs in its source lead has an output resistance Ro = (1+gmRS)ro. The corresponding formula for the BJT case is Ro = [1+gm(Re||rp)]ro.
Biasing in integrated circuits utilizes current sources. As well, current sources are used as load devices. Typically an accurate and stable reference current is generated and then replicated to provide bias current for the various amplifier stages on the chip. The heart of the current-steering circuitry utilized to perform this function is the current mirror.

## Slide 22
Quiz 2.6
a) A power supply VDD = 3.3V, VGS = 1.2V and IREF = 120μA. Q1 and Q2 have k’n = 200 μA/V2, threshold voltages Vt1 = Vt2 = 0.8V.
Determine R.
Determine threshold voltage (W/L)1.
If Io = 100μA, find (W/L)2.
You submit your solution not later than March 20, 2020.
You can submit through Blackboard as informed by Mr. Huy on Blackboard announcement.
b) A BJT current mirror depicted in the Figure has the power supply V1 = 5V, VBE = 0.7V corresponding to working current. Q1 and Q2 are matched and β = 100 .
Determine R1 to obtain IIN = 2mA.
Determine approximated value of Io.