## Slide 1
Text book:
Sedra and Smith, “Microelectronic Circuits,” 6th Edition.
Lecture # 3: Differential & Multistage Amplifiers
International University
School of Electrical Engineering
ANALOG ELECTRONICS

## Slide 2: Content
The BJT differential pair
Small-signal operation of the BJT differential amplifier
Other non-ideal characteristics of the differential amplifier
MOS differential amplifiers
Biasing in integrated circuits
The BJT differential amplifier with active load
Multistage amplifiers

## Slide 3: Introduction
The differential amplifier (pair) configuration is the most widely used building block in analog IC design.
BJT differential amplifier is the basis of a very-high-speed logic circuit family, called emitter-coupled logic (ECL).

## Slide 5: Introduction
There are 2 reasons for using differential in preference to single-ended amplifiers.
(1) Differential circuits are much less sensitive to noise and interference than single-ended circuits.
(2) It enables us to bias the amplifier and to couple amplifier stage without the need of bypass and coupling capacitors which are impossible to fabricate economically by IC technology.
Advantages

## Slide 6: The BJT Differential Pair Basic Operation-1:Common-mode input
The differential pair with a common-mode input signal vCM.
Two transistors are matched.
Current source with infinite output resistance.
Current I divide equally between two transistors.
The difference in voltage between the two collector is zero.
The differential pair rejects the common-mode input signal as long as two transistors remain in active region.

## Slide 7: The BJT Differential Pair Basic Operation-2
The differential pair with a “large” differential input signal.
Q1 is on and Q2 is off.
Current I entirely flows in Q1.

## Slide 8: The BJT Differential Pair Basic Operation-3
The differential pair with a large differential input signal of polarity opposite to that in (b).
Q2 is on and Q1 is off.
Current I entirely flows in Q2.

## Slide 9: The BJT Differential Pair Basic Operation-4:Difference-mode or Difference signals
The differential pair with a small differential input signal vi.
Small signal operation or linear amplifier.
Assuming the bias current source I to be ideal and thus I remains constant with the change in vCM.
Increment in Q1 and decrement in Q2.

## Slide 10: EXERCISE 1
Find vE, vC1, and vC2 in the circuit of Fig.. Assume that |vBE| of a conducting transistor is approximately 0.7 V and that α  1.

## Slide 11: EXERCISE 1 – Sol.
Key point: Which Transistor is ON?
Q2 is ON, Why?

## Slide 12
Quiz 3.1
a) Fig. 1 shows a power supply VCC = 10V, IEE = 2mA, RC = 4kΩ, Vin1 = Vin2 = 3V, α=0.98. Q1 and Q2 are matched.
Determine VP.
Determine Vout1 and Vout2 and deduce Vout.
The input signal in this question is common or differential modes?
You submit your solution not later than March 27, 2020.
b) Fig. 1 shows a power supply VCC = 10V, IEE = 2mA, RC = 2kΩ, Vin1 = 2V
Vin2 = 3V, α=0.98. Q1 and Q2 are matched.
Determine VP.
Determine Vout1 and Vout2 and deduce Vout.
If the current source IEE is connected to – 5V (not Ground), what is the value of VP.
Fig. 1