## Slide 1: Small-signal operation of the BJT differential amplifier
The currents and voltages in the differential amplifier when a small differential input signal vid is applied.
gm = IC/VT
ic = gmvi

## Slide 2: Small-Signal Operation
A simple technique for determining the signal currents in a differential amplifier excited by a differential voltage signal vid; dc quantities are not shown.
ib = ie/(β+1)

## Slide 3: Small-Signal Operation
A differential amplifier with emitter resistances.
Only signal quantities are shown (in color).

## Slide 4: Input Differential Resistance
The resistance seen between the two bases is equal to the total resistance in the emitter circuit multiplied by (1+β).
Input differential resistance of differential pair with emitter resistors.

## Slide 5: Differential Voltage Gain
Differential voltage gain
  Output voltage taken single-ended
  Output voltage taken differentially

## Slide 6: Differential Voltage Gain
Differential voltage gain of the differential pair with resistances in the emitter loads
  Output voltage taken single-ended
  Output voltage taken differentially
  The voltage gain is equal to the ratio of the total resistance in the collector circuit (α to the total resistance in the emitter circuit.

## Slide 7: Differential Half-Circuit Analysis
Differential input signals.
Single voltage at joint emitters is zero (AC ground).
The circuit is symmetric.
Equivalent common-emitter amplifiers in (b).

## Slide 8: Differential Half-Circuit Analysis
This equivalence applies only for differential input signals.
Either of the two common-emitter amplifiers can be used to find the differential gain, differential input resistance, frequency response, and so on
Half circuit is biased at I/2.
The voltage gain(with the output taken differentially) is equal to the voltage of half circuit.
(vc2-vc1)/vid =
(1+β)2re

## Slide 9: Differential Half-Circuit Analysis
The differential amplifier fed in a single-ended manner.
Signal voltage at the emitter is not zero.
Almost identical to the symmetric one.

## Slide 10: Common-Mode Gain
The differential amplifier fed by a common-mode voltage signal vicm.

## Slide 11: Common-Mode Gain
Equivalent “half-circuits” for
common-mode calculations.
  Reminder:
  The voltage gain is equal to the ratio of the total resistance in the collector circuit (α to the total resistance in the emitter circuit.

## Slide 12: Common-Mode Gain
Common-mode voltage gain
  Output voltage taken single-ended (if α1 and REE>>re)
  Output voltage taken differentially
(*)
vicm
Common mode signals cannot be amplified
(**)

## Slide 13: Common-Mode Rejection Ratio
Common-mode rejection ratio
  Output voltage taken single-ended
  Output voltage taken differentially
  This is true only when the circuit is symmetric.
Mismatch on CMRR
REE
( ACM = 0 as **)
(ACM is computed as *)
Proof: We assume that Rc in Acm1 expression becomes RC+∆RC and RC in Acm2 expression does not change. Then we compute Acm shown in formula above.

## Slide 14: Input Common-Mode Resistance
Definition of the input common-mode resistance Ricm.
The equivalent common-mode half-circuit.
Input common-mode resistance is very large.

## Slide 15: Example 1

## Slide 16: Example 1 (cont’d)
The differential amplifier in Fig. uses transistors with β = 100. Evaluate the following:
(a) The input differential resistance Rid .
(b) The overall differential voltage gain vo/ vsig (neglect the effect of ro).
(c) The worst-case common-mode gain if the two collector resistances are accurate to within ±1%.
(d) The CMRR, in dB.
(e) The input common-mode resistance (assuming that the Early voltage VA = 100 V).

## Slide 17: Example 1 – Sol.

## Slide 18
Example 1 – Sol.

## Slide 19
Quiz 3.2
a) Fig. 1 shows a differential amplifier with I = 1mA, RC = 2kΩ, vB1 = - vB2, α = 0.99. Q1 and Q2 are matched.
Find differential voltage gain Ad = (vc2-vc1)/vab where vab = va – vb = vB1 - vB2.
Determine differential input resistance Rab.
What is the common mode gain Ac of this circuit? What is CMRR?
Fig. 1
-VEE
a
b
c
d
o
o
o
o
e
f
g
b) Fig. 1 shows a differential amplifier with I = 1mA, RC = 2kΩ, vB1 = - vB2, α = 0.99. The segments c-a and d-b are replaced by resistance Rsig = 200 Ω. Q1 and Q2 are matched.
Find differential voltage gain Ad = (vc2-vc1)/vab where vab = va – vb
Find vab/vcd.
Find overall differential voltage gain Av = (vc2-vc1)/vcd where vcd = vc – vd = vB1 - vB2.
What is the common mode gain Ac of this circuit? What is CMRR?

## Slide 20
c) Fig. 1 shows a differential amplifier with I = 1mA, RC = 2kΩ, vB1 = - vB2, α = 0.99. The segments c-a and d-b are replaced by resistance Rsig = 200 Ω. The segments e-g and f-g are replaced by RE = 50 Ω. Q1 and Q2 are matched.
Find differential voltage gain Ad = (vc2-vc1)/vab where vab = va – vb
Find vab/vcd.
Find overall differential voltage gain Av = (vc2-vc1)/vcd where vcd = vc – vd = vB1 - vB2.
What is the common mode gain Ac of this circuit? What is CMRR?
Fig. 2
d) Fig. 2 shows a differential amplifier where the biasing circuit (DC circuit) is not shown. RC = 4kΩ, REE = 100kΩ, re1 = re2 = 50 Ω and α = 0.99. Q1 and Q2 are matched.
Find differential voltage gain Ad = (vc2-vc1)/vid.
If the actual value of RC is specified to be within plus or minus 10% of the nominal value (4kΩ), find the common mode gain Ac.
Compute CMRR in dB?
You submit your solution not later than March 27, 2020.

## Slide 21
You submit your solution not later than March 27, 2020.
Fig. 2
d) Fig. 2 shows a differential amplifier where the biasing circuit (DC circuit) is not shown. RC = 4kΩ, REE = 100kΩ, re1 = re2 = 50 Ω and α = 0.99. Q1 and Q2 are matched.
Find differential voltage gain Ad = (vc2-vc1)/vid.
If the actual value of RC is specified to be within plus or minus 10% of the nominal value (4kΩ), find the common mode gain Ac.
Compute CMRR in dB?